# Title
## Check polarity of silkscreen markings

The PCB has a silkscreen marking that depicts the coordenant system.
The straight arrows point to acceleration direction that results in positively measured acceleration.
The curved arrors are unclear. Use the right hand rule to determine rotation direction that measures as a positive rate of change.

Procedure:
1. Load the minimalist example.
2. Move the IMU throught the 6 axis.

Criteria:
Are the polarities correct? YES

## Check the signal integrity of the I2C lines
Procedure:
1. Socket EUT In breadboard
2. Fly wires to redboard using 6" ended cables (like in SIK)
3. Capture scopes shots of I2C signal and clock, running messages at fastest mode. (100kHz)
4. Capture scopes shots of I2C signal and clock with two I2C loads
Criteria:
1. Does the signal rise in a sufficiently small time? What is it? 480ns
2. Is the clock running at 100kHz YES
3. Does the signal signal rise and fall monotonicly? YES
Test Pictures:

Single I2C load
Dual I2C load
Rise Times

## Check the signal integrity of the SPI lines
Procedure:
1. Socket EUT In breadboard
2. Socket BOB-12009 level shifter into breadboard
3. Connect up power and 4 signal wires to the shifter with 1 inch wires.
4. Fly wires to redboard using 6" ended cables
5. Capture scopes shots of SPI messages at highest speed possible. Inspect between level shifter and EUT.
Criteria:
1. Is data changed on the falling edge? YES
2. Does the signal signal rise and fall monotonicly? YES
3. Does the signal shape look square? YES
4. What is the clock frequency measured? 4.032MHz
Test Pictures:
Message (READ op, addr 0x28 (First data reg), reading 0xFFE9, int16: -23
Zoom in, data changes on falling edge.
## Power Consumption
Procedure:
1. Measure the idling current consumption while connected to a 3.3v MCU
2. Measure the current consumption during fastest FIFO operation possible (SPI_MODE)
## Response to over-volt condition
This test is destructive, do it last
Procedure:
1. Operate the EUT at the hightest bus load possible and at 3.3v.
2. Step the supply voltage up while monitoring and recording current. As so as a runaway condition starts, remove power. If possible, vary the bus voltage with the supply voltage.
3. Run the I2C mode straight from a 5v arduino.
4. Run the SPI mode straight from a 5v arduino.